## Slide 1
1Bartolomeo Viticchiè, 1Mounir Lekouara, 1Marcel Dobber,
1Claude Ledez, 1Gary Fowler, 1Katja Hungershoefer & 2Philip Willemsen
1EUMETSAT, Germany
2ESA ESTEC, The Netherlands
Meteosat Third Generation Lightning Imager performance assessment

## Slide 2: Outline
Meteosat Third Generation program
LI instrument
  Development status
  Detection principle and DT data
LI data processing and Reference Processor
  Level 0
  Level 1b
  Level 2
LI performance assessment
  Pre-launch
  In-orbit
Summary and future activities

## Slide 3: MTG-I imaging mission
Imagery mission implemented by two MTG-I satellites
Full disc imagery every 10 minutes in 16 bands (FCI)
Fast imagery of Europe every 2.5 minutes (FCI)
New Lightning Imager (LI)
Start of operations in 2021
Operational exploitation: 2021-2042
Thales Alenia Space France is the MTG-I prime and Leonardo Italy is the instrument supplier

## Slide 4: MTG-S sounding mission
Hyperspectral infrared sounding mission (IRS)
3D weather cube: temperature, water vapor, O3, every 30 minutes over Europe
Air quality monitoring and atmospheric chemistry in synergy with Copernicus Sentinel-4 instrument (UVN)
Start of operations in 2023
Operational exploitation: 2023-2042

## Slide 5: MTG full operational configuration
MTG-I in Rapid Scan Service on EUMETSAT member states
MTG-I in Full Scan Service
MTG-S Sounding Service

## Slide 6: MTG-I + MTG-S: 4D weather cube
Lightning
Convection
Winds
Atmosphere

## Slide 7: LI instrument development status
LI Optical Head Structural Model and Thermal Model test campaigns completed
Telescope Qualification Model test campaign completed
Flight hardware procurement completed
LI Main Electronic (LME) and Optical Head (LOH) Flight Model integration started
Selected detector units already delivered to instrument manufacturer
Detector characterization tests on-going
  QE well above specification (spec at 70 %)
  Noise parameters well within specification
Instrument Engineering Model (EM) testing on-going
Lower level CDRs closed; the instrument CDR is currently on-going
LI Optical Head Thermal Model
LI telescope Validation Model

## Slide 8: LI instrument and detection principle
LI in a nutshell | 
Spatial Resolution at Nadir | 4.5 km (variable throughout the Filed of View, FOV)
Spectral band | 1.9 nm narrow band
Detector(s) | 1000 x 1170 pixel (x 4) CMOS operated at 293 K
Frame rate | 1 ms (1 kHz acquisition frequency)
Background | 4 navigated images produced every 30 sec (baseline)
Data bandwidth | 30 Mbps (fully exploited) Radiometric noise Micro-vibrations 3x3 window for measurement and background
Mass and Power | 110 kg and 300 W
On-board processing | Background subtraction On-board filtering  to match the bandwidth

## Slide 9: LI instrument and detection principle
LI in a nutshell | 
Spatial Resolution at Nadir | 4.5 km (variable throughout the Filed of View, FOV)
Spectral band | 1.9 nm narrow band
Detector(s) | 1000 x 1170 pixel (x 4) CMOS operated at 293 K
Frame rate | 1 ms (1 kHz acquisition frequency)
Background | 4 navigated images produced every 30 sec (baseline)
Data bandwidth | 30 Mbps (fully exploited) Radiometric noise Micro-vibrations 3x3 window for measurement and background
Mass and Power | 110 kg and 300 W
On-board processing | Background subtraction On-board filtering  to match the bandwidth

## Slide 10: LI instrument and detection principle
Sources of false transients:
Radiometric noise;
Micro–vibration of the platform;
particle impacts on the focal plane;
Sun glint;
…
Typical pixel signal
Background removal and detection threshold computation
Detection (ideal case)
Detection (real case)

## Slide 11: LI instrument DT data
Sources of false transients:
local fluctuations of the radiometric noise;
micro – vibration of the platform;
particle impacts on the focal plane;
Sun glint;
…
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
For each DT:
3x3 window with measurement ()
3x3 window with the estimated background measurement ()
Location in space (lat/lon) and time
This is all it is processed at L0, L1, and L2
False DT
True DT
Time
Radiation
Energy
at 777.4 nm
Night
Day

## Slide 12: LI data processing
EUM: EUMETSAT
ESA: European Space Agency
LDO: Leonardo
TAS: Thales Alenia Space
LI instrument
detection and filtering
Level 1b
processor
Level 2
processor
ESA and LDO
Design: ESA, EUM, and LDO
Operational implementation: TAS and EUM
Design: EUM
Operational implementation: Thales and EUM
Here is where the detection takes place

## Slide 13: LI data processing in the end-to-end Reference Processor (RP)
Instrument simulator
Level 1b
prototype processor
Level 2
prototype processor
Simulated scene
Simulated Level 2 data
Inputs:
Modified SEVIRI VIS0.8 background
Simulated optical pulses
Observation geometry
Micro-Vibration
Radiometric detection including noise
Real Time Pixel Processor (RTPP) detection
Single detection filter (SDT)
Micro-Vibration filter (MVF)
Level 1b background radiometric processing
Level 1b DT radiometric processing
Level 1b DT on-ground filtering:
  pre-processor (sanity checks)
  jitter reconstruction filter
  spatio-temporal coherency filter
  hybrid filter
Simulated Level 0 data
from this step on DTs are organized in groups and flashes
DT acceptance for Level 2 processing
Group computation
Group filtering
Flash computation
Flash filtering
Flash accumulation
Simulated Level 1b data
Here is where the detection takes place

## Slide 14: One example
30 sec simulation over central Europe
Flash “seeds” from GLD360
Properties of pulses in flashes derived from LIS statistics
Minimum required detectable pulse size and energy (from LI System Requirements)
Visualization through a prototype of the LI Processing Visualization Tool (LI PVT)

## Slide 15: Simulation input
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 16: DTs at Level 0 RTPP
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 17: DTs at Level 0 RTPP
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
Single Detection (DT) Filter (SDTF): check the content of the 8 neighbors
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 18: DTs at Level 0 RTPP
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 19: DTs at Level 0 SDTF
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 20: DTs at Level 0 SDTF
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product
Type equation here.
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
Micro Vibration Filter (MVF): check the background gradient

## Slide 21: DTs at Level 0 SDTF
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 22: DTs at Level 0 MVF
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 23: LI data processing in the end-to-end Reference Processor (RP)
Instrument simulator
Level 1b
prototype processor
Level 2
prototype processor
Simulated scene
Simulated Level 2 data
Inputs:
Modified SEVIRI VIS0.8 background
Simulated optical pulses
Observation geometry
Micro-Vibration
Radiometric detection including noise
Real Time Pixel Processor (RTPP) detection
Single detection filter (SDT)
Micro-Vibration filter (MVF)
Level 1b background radiometric processing
Level 1b DT radiometric processing
Level 1b DT on-ground filtering:
  pre-processor (sanity checks)
  jitter reconstruction filter
  spatio-temporal coherency filter
  hybrid filter
Simulated Level 0 data
from this step on DTs are organized in groups and flashes
DT acceptance for Level2 processing
Group computation
Group filtering
Flash computation
Flash filtering
Flash accumulation
Simulated Level 1b data
Properties of the single DTs and their background (including windows) over 1 ms

## Slide 24: DTs to be processed on-ground (Level 0 data)
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 25: DTs at Level 1b pre-processing
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 26: DTs at Level 1b pre-processing
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product
Type equation here.
Hybrid Filter (HYB): combined check on the margin with which the on-board SDTF and RTPP conditions were passed.
If the margin at SDTF is larger than a threshold the DT is classified as true.
If the margin at SDTF is smaller than the threshold the check is done on the margin at RTPP. If the test is passed the DT is classified as true.
If the margin at RTPP is also smaller than a threshold a [0, 1] descriptor for the DT is computed: 1 meaning certainly false DT according to the filter.

## Slide 27: DTs at Level 1b pre-processing
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 28: DTs at Level 1b HYB
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 29: DTs at Level 1b HYB
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product
Type equation here.
Jitter-Reconstruction Filter (JIT):
Computation for all the DTs of the ratio between the lightning signal (i.e., ) and the background gradient.
Individuation of “beacons” with particularly low ratio.
Estimation of the jitter movement from the “beacons” properties.
Computation of a corrected value .
New RTPP detection run to see if the clean-from-jitter measurements would have passed the detection; the outcome is provided with a [0, 1] descriptor.

## Slide 30: DTs at Level 1b HYB
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 31: DTs at Level 1b JIT
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 32: DTs at Level 1b JIT
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product
Type equation here.
Spatio-Temporal Coherency Filter (STC): check on the correlation between each DT and the other DTs in a spatio-temporal window of 0.5 sec (rolling window) and 50 km respectively.

## Slide 33: DTs at Level 1b JIT
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 34: DTs at Level 1b STC
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 35: LI data processing in the end-to-end Reference Processor (RP)
Instrument simulator
Level 1b
prototype processor
Level 2
prototype processor
Simulated scene
Simulated Level 2 data
Inputs:
Modified SEVIRI VIS0.8 background
Simulated optical pulses
Observation geometry
Micro-Vibration
Radiometric detection including noise
Real Time Pixel Processor (RTPP) detection
Single detection filter (SDT)
Micro-Vibration filter (MVF)
Level 1b background radiometric processing
Level 1b DT radiometric processing
Level 1b DT on-ground filtering:
  pre-processor (sanity checks)
  jitter reconstruction filter
  spatio-temporal coherency filter
  hybrid filter
Simulated Level 0 data
from this step on DTs are organized in groups and flashes
DT acceptance for Level2 processing
Group computation
Group filtering
Flash computation
Flash filtering
Flash accumulation
Simulated Level 1b data
Properties of a buffer of DTs and their background accumulated over 1 sec

## Slide 36: LI Level 2 processing (1 of 2)

## Slide 37: LI Level 2 processing (2 of 2)

## Slide 38: DTs at Level 1b STC
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 39: DTs at Level 2
purple = location of input pulses
cyan = DTs through Level 0 proc.
green = DTs through Level 1b proc.
orange = DTs in the Level 2 product

## Slide 40: Level 2 Accumulated Product

## Slide 41: Level 2 Accumulated Product (ZOOM IN)

## Slide 42: LI data processing in the end-to-end Reference Processor (RP)
Instrument simulator
Level 1b
prototype processor
Level 2
prototype processor
Simulated scene
Simulated Level 2 data
Inputs:
Modified SEVIRI VIS0.8 background
Simulated optical pulses
Observation geometry
Micro-Vibration
Radiometric detection including noise
Real Time Pixel Processor (RTPP) detection
Single detection filter (SDT)
Micro-Vibration filter (MVF)
Level 1b background radiometric processing
Level 1b DT radiometric processing
Level 1b DT on-ground filtering:
  pre-processor (sanity checks)
  jitter reconstruction filter
  spatio-temporal coherency filter
  hybrid filter
Simulated Level 0 data
from this step on DTs are organized in groups and flashes
DT acceptance for Level2 processing
Group computation
Group filtering
Flash computation
Flash filtering
Flash accumulation
Simulated Level 1b data
Properties of DTs organized in groups and flashes and their background

## Slide 43: LI data processing in the end-to-end Reference Processor (RP)
Instrument simulator
Level 1b
prototype processor
Level 2
prototype processor
Simulated scene
Simulated Level 2 data
Inputs:
Modified SEVIRI VIS0.8 background
Simulated optical pulses
Observation geometry
Micro-Vibration
Radiometric detection including noise
Real Time Pixel Processor (RTPP) detection
Single detection filter (SDT)
Micro-Vibration filter (MVF)
Level 1b background radiometric processing
Level 1b DT radiometric processing
Level 1b DT on-ground filtering:
  pre-processor (sanity checks)
  jitter reconstruction filter
  spatio-temporal coherency filter
  hybrid filter
Simulated Level 0 data
from this step on DTs are organized in groups and flashes
DT acceptance for Level2 processing
Group computation
Group filtering
Flash computation
Flash filtering
Flash accumulation
Simulated Level 1b data
Level 2 Groups
Level 2 Flashes
Level 2 Accumulated Products

## Slide 44: LI performance assessment
Pre-launch assessment (end-to-end)
  Based on simulations (LI Reference Processor)
  Complementary to the industry assessment
In-orbit assessment, i.e., LI Commissioning and long-term monitoring
  Based on Offline Tools (OFTs)
  Complementary to the industry assessment

## Slide 45: LI performance assessment – pre-launch
  Based on simulations
  Complementary to the industry assessment
Industry settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Random in space (sub-pixel) and time (wrt the frame central time); the locations are picked within the cloud mask by keeping a uniform angular distribution from the sub-satellite point
Processing level | Level 1b

## Slide 46: LI performance assessment – pre-launch
  Based on simulations
  Complementary to the industry assessment
Industry settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Random in space (sub-pixel) and time (wrt the frame central time); the locations are picked within the cloud mask by keeping a uniform angular distribution from the sub-satellite point
Processing phase | Level 1b

## Slide 47: LI performance assessment – pre-launch
EUMETSAT settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Within flashes whose barycentre location is random in space and time (same as above for pulses)
Flash properties | Groups in flashes (LIS based) Δt between groups (LIS based) Δd between groups (random within 5 km radius) Random location around the barycentre
Processing level | Level 2

## Slide 48: LI performance assessment – pre-launch
EUMETSAT settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Within flashes whose barycentre location is random in space and time (same as above for pulses)
Flash properties | Groups in flashes (LIS based) Δt between groups (LIS based) Δd between groups (random within 5 km radius) Random location around the barycentre
Processing phase | Level 2

## Slide 49: LI performance assessment – pre-launch
EUMETSAT settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Within flashes whose barycentre location is random in space and time (same as above for pulses)
Flash properties | Groups in flashes (LIS based) Δt between groups (LIS based) Δd between groups (random within 5 km radius) Random location around the barycentre
Processing phase | Level 2

## Slide 50: LI performance assessment – pre-launch
EUMETSAT settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Within flashes whose barycentre location is random in space and time (same as above for pulses)
Flash properties | Groups in flashes (LIS based) Δt between groups (LIS based) Δd between groups (random within 5 km radius) Random location around the barycentre
Processing phase | Level 2
PROS:
treat each single flash separately  EASY COMPUTATION OF FLASH DE FROM THE INPUT
simultaneous flashes within the LI FOV  MULTIPLE DETECTION CONDITIONS
duration of simulations comparable to typical flash duration  SHORT SIMULATIONS
CONS:
Not representative of flashes correlated in space and time within storms
Cannot be used to produce long sequences of test data

## Slide 51: LI performance assessment – pre-launch
EUMETSAT settings | 
Background | 3 scenarios representative of: Full illumination Night Day-night terminator
Pulse energy | Minimum required detectable energy (function of the local background)
Pulse radius | 5 km (fixed)
Pulse duration | 0.6 millisecond
Pulse location | Within flashes whose barycentre location is random in space and time (same as above for pulses)
Flash properties | Groups in flashes (LIS based) Δt between groups (LIS based) Δd between groups (random within 5 km radius) Random location around the barycentre
Processing phase | Level 2
PROS:
treat each single flash separately  EASY COMPUTATION OF FLASH DE FROM THE INPUT
simultaneous flashes within the LI FOV  MULTIPLE DETECTION CONDITIONS
duration of simulations comparable to typical flash duration  SHORT SIMULATIONS
CONS:
Not representative of flashes correlated in space and time within storms
Cannot be used to produce long sequences of test data
SPACE OF SETTINGS TO RUN AN ENSEMBLE OF SIMULATIONS AIMED AT ASSESSING:
Level 1b AND Level 2 DETECTION PERFORMANCES IN A ROBUST WAY
THE DEPENDENCY OF THE PERFORMANCES ON THE CHANGE OF INPUT SETTINGS  IN DEPTH KNOWLEDGE OF LI PERFORMANCES

## Slide 52: LI performance assessment – in-orbit
  In October 2018 EUMETSAT kicked-off the preparation of the LI System Commissioning
Following the "Satellite" commissioning (satellite + prototype processor) by ESA and industry, EUMETSAT will perform the System Commissioning (satellite + operational processor) to assess the system readiness to deliver validated L2 products to the End Users
EUMETSAT has defined the specifications of the different tests aimed at verifying the system requirements
In parallel, the so called Offline Tools (OFTs) that will be employed for performing the verification (i.e., the software) have been specified

## Slide 53: LI performance assessment – in-orbit
LI instrument
detection and filtering
Level 1b
Instrument Data Processing Facility
Level 2
L2 Processing Facility
Level 1b DTs and background
Level 2 products
Level 0 data
IQT: Image Quality Tool
L1PP: Level 1 Prototype Processor
PAT: Performance Assessment Tool
IQT = L1PP + PAT
ESA

## Slide 54: LI performance assessment – in-orbit
LI instrument
detection and filtering
Level 1b
Instrument Data Processing Facility
Level 2
L2 Processing Facility
Level 1b DTs and background
Level 2 products
Level 0 data
LI PVT
SIFT
PIQMICS
MICMICS
FCI Level 1c and 2 products
LLs external data
PIQMICS: Performance Image Quality MonItoring and Characterization System
MICMICS: Mission Integrated Calibration Monitoring Inter-Calibration System
SIFT: Satellite Information Familiarization Tool (https://sift.ssec.wisc.edu/)
LI PVT: LI Processing Visualization Tool
LI-STAR: LI STAtistics and Reporting
LLs: Lightning Location Systems
Performance DBs
LI-STAR
EUMETSAT

## Slide 55: LI performance assessment – in-orbit
LI-STAR | 
Requirement | Test Description
Pulse DE | LI L2 group-to-Ref stroke/group matching against external LLs data
Flash DE | LI L2 flash-to-Ref stroke/flash matching against external LLs data
FAR/Flash FAR | Identification of storm regions by means of LI L2 data and external LLs data and identification of outliers, i.e., false detections/flashes
LLs external data
Europe: ATDnet, EUCLID, LMAs in Spain and France
South America and Atlantic Ocean: GLM on GOES-East
LI FOV: GLD360 and ISS-LIS
Coordinated effort
EUMETSAT + LI Mission Advisory Group
KEY ROLE OF US EXPERTS

## Slide 56: LI performance assessment – in-orbit
MICMICS | 
Requirement | Test Description
Radiometric accuracy | Moon calibration
 | Vicarious calibration through desert targets (absolute calibration)
 | Deep Convective Clouds (DCC) calibration
 | Intra-OC analysis on the different overlap areas (histogram and pixel-based)
 | LI vs FCI pixel-based analysis

## Slide 57: LI performance assessment – in-orbit
PIQMICS | 
Requirement | Test Description
Geometric accuracy (ASPKE) | Landmark analysis
 | Star matching
 | Intra-OC analysis (based on tie points and landmark)
 | LI vs FCI pixel-based analysis (co-registration over land regions)
 | Complementary: lightning navigation and timing accuracy against external LLs data
A total of 41 tests are currently planned for the LI Commissioning and long-term monitoring:
Data timeliness and format (from Level 0 to Level 2);
Data quality and processing load
Instrument performance and characterization

## Slide 58: Summary and future activities
LI preparation is on-going in view of the launch in late 2021
Focus on the LI performance assessment
  Pre-launch:
    based on simulations through the LI Reference Processor
    Plan to perform a systematic analysis of the LI performance from an wide range of input conditions
    Plan to perform a Level 2 tuning exercise on simulated data
  In-orbit:
    The LI Commissioning Test Specifications have been completed
    The definition of an in-flight tuning strategy will start in September 2019
    The definition of the LI System Commissioning schedule will start in November 2019
    The implementation of the LI Offline Tools for System Commissioning has been kicked-off in August 2019