## Slide 1
A satellite mission concept for multispectral, 3-D observations of lightning
CubeSpark
Patrick Gatlin, Timothy Lang, Mason Quick, NASA Marshall Space Flight Center
Sonja Behnke, Los Alamos National Laboratory
2021 GLM Science Team Meeting
Notes: Background Image credit: ISS Crew Earth Observations Facility and the Earth Science and Remote Sensing Unit, Johnson Space Center (Image ISS042-E-135030; Cyclone Bansi, Indian Ocean, January 25, 2015 taken with ISS Digital Camera by Expedition 42 Crew; https://eol.jsc.nasa.gov/SearchPhotos/photo.pl?mission=ISS042&roll=E&frame=135030)

## Slide 2: Combining optical and RF to get novel 3-D observations

## Slide 3: Why are 3-D observations of lightning important?
Thundercloud processes, charge structure and Severe weather
depiction of LNOx PRODUCTION and distribution in troposphere
Vertical information provides key insights about thundercloud effects on its surrounding environment
(Koshak et al. 2014)
(Liaskos et al. 2015)
LNOx effects on Energy Budget
Ozone increase in Boundary Layer due to LNOx
(Gatlin & Goodman 2010)
Vertical growth as storm intensifies
Lightning in Overshooting Tops
(Calhoun et al. 2013)
(Lang et al. 2011)
Anomalous Charge Storms and Flash Type/Polarity
(Fuchs et al. 2018)
Kinematic/Microphysical Processes
(Davis et al. 2019)
Transport of LNOx

## Slide 4: Need to detect small and low-altitude flashes important for diagnosing storm intensification and severe weather
?
(Mason Quick)
(Zhang & Cummins 2020)
GLM vs KSCLMA Detection
(Rutledge et al. 2020)
GLM vs COLMA
Short-lived, small flashes difficult to detect with coarse resolution imagers like GLM and LIS
Low-altitude lightning flashes tend to elude optical detection from space
Deficiencies mask important processes related to the development of severe weather
Need to better resolve unknown characteristics of lightning optical emissions from thunderstorms on Earth

## Slide 5: How can we detect flash activity that evades current imagers?
(ASIM/MMIA analysis by P. Bitzer & D. Walker)
Cool (streamer) processes often seen during early stages of flash development can produce 337-nm (UV) emissions that may not be detectable in the 777.4-nm, as shown by ASIM-MMIA
Increasing the horizontal resolution should improve detection of smaller flashes, as suggested by FEGS comparisons with LIS/GLM
Since lightning’s optical emissions are impacted by water pathways through the cloud, we can exploit its RF emissions, which are impacted by the ionosphere but detectable in space by monitoring VHF frequencies (numerous FORTE findings summarized in Light 2020)
  Impulsive VHF events detected by FORTE are optically weak
  Enables vertical location of lightning sources
(Peterson et al. 2021)
VHF+Optical Detections with FORTE
Group Radiance
Group Area
FEGS
Area vs Radiance
LIS
FEGS
GLM

## Slide 6: CubeSpark will use a novel approach to address outstanding questions about thunderstorm processes and effects on the surrounding environment
How does the altitude of lightning impact detection of its optical signatures at cloud top?
How does the vertical distribution of lightning relate to processes of thundercloud environments and occurrence of severe weather?
What is the global distribution of anomalously charged thunderstorms, their relationship to severe weather, and impact on LNOx?
What is the distribution of LNOx in the troposphere and its relation to ozone variability?
What is the vertical structure of winter-storm lightning, and how does it relate to human-built structures?
CubeSpark Approach
Constellation of 6 satellites in LEO
Each satellite will have an RF payload to detect lightning in VHF
At least 2 of the satellites will have high-resolution, NIR/UV CMOS cameras
Event detection will be performed onboard and sent to ground
Use optical to constrain the TOA solutions for 3D geolocation
Measurement Requirements
Locate the horizontal and vertical origin of lightning events with an uncertainty ≤2-km (1-km goal)
Measure the 777.4- and 337-nm optical emissions at cloud-top with 1-2-km resolution every 0.5-1-ms
Detect greater fraction of lightning activity in severe storms than current imagers (e.g., DE>60% in severe storms)

## Slide 7: Feasibility of meeting 1-2-km location retrieval uncertainties?
Modified LMAsimulation code (Chmielewski & Bruning, 2016):
6 VHF receivers at LEO altitudes (timing uncertainty 500-ns)
Included basic ionospheric propagation model to get added timing uncertainty
Varied the network geometry to examine location uncertainties
HOW DOES THIS CHANGE GIVEN ORBITAL MECHANICS?
Horizontal uncertainties<<1-km
Vertical uncertainties <2-km for altitudes <600-km and satellites spaced >~300-km apart on orbital plane
Initial orbital configuration of sensors
Snaphot of simulated location uncertainties
1-km
2-km
Orbital Altitude?
Vertical RMS error [m]
Satellite Spacing?
525-km altitude
Orbital planes 400-km apart
Vertical RMS error [m]
1-km Goal
2-km Req.
Simulations performed by Sarah Stough

## Slide 8: Orbital Simulations
R. Hopkins (MSFC ED04)
 Coverage and Uncertainty (i.e., RMS) of location retrievals will vary with latitude

## Slide 9: Which constellation design will provide the most coverage with lowest uncertainty?
Distance from Equator
Option #1
Option #2
Distance from Equator
Option #3
Distance from Equator
Latitude | Option #1 | Option #2 | Option #3
0° | 2.8-km | 1.3-km | N/A
30° | 3.2-km | 2.0-km | 5.3-km
60° | 3.4-km | 5.9-km | 1.8-km
Vertical uncertainty from orbital TOA simulations
Area (FOV) of robust 3-D retrievals

## Slide 10: Remaining questions and technical hurdles
(FEGS analysis by Mason Quick)
Is the CMOS sensor sensitive enough to the optical emission with a 0.5-1 ms integration time?
  MSFC is testing a candidate sensor from e2V for use in CLIDE
How much lightning can be detected at 337- and not 777.4-nm and what are the UV characteristics of lightning?
  Ongoing MMIA analysis
Can the size and complexity of the lens assembly be reduced while maintaining the same ultra-narrow bandpass filter performance?
  Apply a uniform filter coating to a semi-hemispheric lens
Higher resolution images will require a new data acquisition approach
  Use AI to define regions of interest for enhanced observation
What type of and how much lightning activity can be detected with an orbital VHF receiver?
  ACT project with LANL includes comparing LMA with FORTE
Does an optical-based location constrain the space-based TOA solution such that ≤2-km vertical resolution can be achieved using fewer independent VHF measurements?
  NPP fellow (Jackson Remington) starting in Nov/Dec to work on this
Adding UV filter to FEGS
Patrick.Gatlin@nasa.gov