## Slide 1: GOES-18 GLM Instrument Performance and Optimization
September 2022
GLM Science Meeting
© 2022 Lockheed Martin Corporation. All Rights Reserved.
Tewa Kpulun
This presentation was made possible by work performed under NASA contract NNGO8HZOOC

## Slide 2: Timeline of Major Instrument PLT Events
Raw First Light Image
Mar Apr May Jun Jul Aug Sep Oct Nov
Launch
Activation
Outgas
Door Deployment
First Light
All ground LUTs updated
All on orbit parameters set
Eclipse
G18 PLT is on schedule according to the planned sequence of events
Spacecraft Drift

## Slide 3: Changes since GOES-17
Hardware changes between FM2 (GOES-17) and FM3 (GOES-18)
  Stray light mitigation
    G18 BG image intensity during solar intrusion is 10 to 40% less than G17, depending on FOV location
  Electronic design modifications
    Reduction of CCD readout artifacts (overshoot)
    Better dynamic range from lower thresholds under high illumination
    Over a 24hr period on August 9th:
      G18 has zero saturated pixels
      G17 has 63,378 saturated pixels
GOES-17
GOES-18
Hardware changes improved dynamic range, by decreasing the number of saturated pixels
Solar Intrusion (sun shining into optics)

## Slide 4: PLT On-orbit Instrument Calibration and Thresholds
Extending the DC restore pulse to a triple-wide coarse waveform lowered the overall instrument noise.
Triple-wide ADC offset settings are sufficient and meet instrument requirements
  Too high: risk saturating the instrument
  Too low: risk of lowering DE during night time
Decrease of the on-board thresholds improves the detection of low energy flashes.
FM3R Double-wide
FM4R Timing H
FM3R Triple-wide
BG pixel statistics for the three different timing settings tested. Slight differences due to scene variation.
Spatial noise analysis done in fast BG during solar midnight.
RTEP Threshold Results

## Slide 5: PLT Navigation Parameters
The coastline ID roll, pitch, and yaw (RPY) values were evaluated by fine tuning the instrument’s magnification parameters:
  Effective focal length (EFL)
    Black arrow are PDR values
  Barrel distortion
Navigation checked using coastline overlay on navigated backgrounds
  Coastline ID convergence is within 1.5 pixel requirement.
  Comparison with GOES-17 GLM shows preliminary agreement
  Extensive navigation validation will occur during provisional PLPT
GOES-17
GOES-18
Lake Okeechobee, FL

## Slide 6: Lightning Detection Prediction
Used lightning data from G18 and G17 around solar noon and solar midnight in the GOES West location
  Solar Noon: 2022-07-28 21:30 to 21:40 Z
  Solar Midnight: 2022-07-28 09:25 to 09:35 Z
Case | Number of Events | Number of Groups | Number of Flashes
 | Full Disk | CONUS | Full Disk | CONUS | Full Disk | CONUS
G17 Noon | 94,640 | 74,225 | 48,923 | 38,960 | 6,698 | 5,267
G18 Noon | 146,695 | 113,907 | 63,895 | 50,666 | 8,087 | 6,151
G17 Midnight | 131,506 | 124,243 | 39,416 | 37,166 | 2,482 | 2,372
G18 Midnight | 200,302 | 188,024 | 59,305 | 55,746 | 2,965 | 2,808
GOES-18 detects more flashes than GOES-17 for both full disk and
  For the time periods above, G18 detects ~15% more flashes than G17
Extensive validation and comparison to ground truth will occur during provisional PLPT

## Slide 7: Future G18 GLM PLT Activities
Cross-satellite comparison testing
Assist ground in implementation and testing of updated GPAs
  e.g. blooming filter
Further event detection and navigation analysis with ground truth systems
  Using ENGLN and GLD360
PLT instrument tuning is complete. On orbit performance is excellent.

## Slide 8
© 2022 Lockheed Martin Corporation. All Rights Reserved.
This presentation was made possible by work performed under NASA contract NNGO8HZOOC