## Slide 1: Developing a Raspberry Pi-based Camera Network and Its Applications
Daile Zhang
CISESS/University of Maryland
CISESS/UMD
CIMSS/OU
Earth Networks
NASA Marshall
Special thanks to Ken Cummins, Doug Baker, and Michael Peterson
Karl Stock
?
Mason Quick
Mike Stock
Vanna
Chmielewski
Jeff Lapierre
Guangyang Fang
Joseph Patton
Terrence Pierce
Domenic Brooks
Alex Friedman
NOAA NA19NES4320002 and CISESS Seeds Grant

## Slide 2
Raspberry Pi cameras
Raspberry Pi cameras and settings
UMD Campus
College Park, MD
Flagstaff, AZ
Earth Networks
Germantown, MD
CISESS/ESSIC
College Park, MD
8 in operation
5 in MD, 2 in AZ, and 1 in OK

## Slide 3: An 8-Stroke CG flash on 20220522 in Germantown,MD
Looking south

## Slide 6: First Strokes – Two Simultaneous Strokes
2 NLDN CG strokes
-11kA and -9kA
2 ENTLN CG strokes
-16.6kA and -15.1kA

## Slide 7: Second Stroke (new leaders/striking point)
A -16kA CG and a 2kA IC
17.7kA CG

## Slide 8: 3rd Stroke (continuing current)
-2kA IC
ENTLN didn't detect anything.

## Slide 9: 4th Stroke
-12kA CG
-14.6kA CG

## Slide 10: 5th Stroke (continuing current)
-3kA IC
-5.3kA CG
NLDN misclassified.

## Slide 11: 6th Stroke (continuing current)
-11kA CG
-11.6kA CG

## Slide 12: 7th Stroke (continuing current)
-8kA IC
-10.0kA CG
NLDN misclassified.

## Slide 13: 8th Stroke (continuing current)
NLDN 20:30:11.116 -3kA IC
ENTLN 20:30:11.116 -5.1kA IC
Video-derived time is 20:30:11.114

## Slide 14: Findings
GLM matched with the video well. GLM detected the first 7 strokes. The 8th stroke was 4-5 ms later than the video (more than 2 ms).
GLM correlated well with the ground-based measurements in both time (within 2 ms temporal resolution) and space (within 1 pixel size), except for the last stroke.
The brightest GLM pixel was not the closest one with the ground-based measurement, but off by one pixel due to parallax.

## Slide 15: Long Continuing Current Flash in Flagstaff 20220801
Looking east

## Slide 16: Regular speed

## Slide 17: Slow-Mo

## Slide 18: Findings
The flash lasted for 45 frames (approx. 500 ms) with long continuing current.
Neither GLM-16 or -17 detected this flash. Nothing within 50 km and 1 second.
ENTLN detected 3 CGs with the first one from WWLLN.
NLDN detected 3 CGs and 3 ICs.
The 3 CGs matched well between ENTLN and NLDN. ENTLN didn’t detect any NLDN ICs.
* Camera time is off by about 177 ms.

## Slide 19: Why GLM Miss Detection?
Strokes with continuing currents tend to be less intense.
Flagstaff, AZ daytime detection threshold is about 2 fJ higher than in Germantown, MD.
(Cummins 2021)

## Slide 20: A 12-stroke (or 13?) Flash on 20220712 in College Park, MD
Looking South

## Slide 22
21:58:52.897
-48.9 kA
-37.8 kA

## Slide 23
21:58:52.960
-17.7 kA
-10.8 kA

## Slide 24
21:58:52.961
-12.4 kA
-10.1 kA

## Slide 25
21:58:53.006
-33.1 kA
-25.6 kA

## Slide 26
21:58:53.069
-39.0 kA
-27.6 kA

## Slide 27
21:58:53.153
-7.6 kA
-4.2 kA
NLDN misclassified.

## Slide 28
21:58:53.232
-27.5 kA
-17.9 kA

## Slide 29
21:58:53.304
-29.9 kA
-19.4 kA

## Slide 30
21:58:53.353
-10.3 kA

## Slide 31
21:58:53.370
-11.1 kA
-6.0 kA

## Slide 32
21:58:53.398
-22.5 kA
-12.4 kA

## Slide 33
21:58:53.452
-18.7 kA
-10.7 kA

## Slide 34
21:58:53.554
-25.0 kA
-14.9 kA

## Slide 35: Findings
GLM only detected 2 frames with one frame around 3 ms (>frame rate) from the ground measurement. First GLM frame only had one lit-up pixel at least 30 km from the ground point. Last GLM frame had two closer pixels around 10-20 km from the ground point. But those pixels didn’t match with the first frame in geolocations.
Both ENTLN and NLDN were able to pick up simultaneous strokes in the first frame. ENTLN detected all 12 strokes with one additional stroke not being caught in the frame. NLDN detected 11 out of 12 strokes with the additional one not in the frame. Matched well both in time and space.

## Slide 36: Why GLM Miss Detection?
Higher reflectivity indicated that abundant of hydrometeors between the cloud top and the flash could increase light scattering.

## Slide 37: Summary
Overall, GLM detected most CG flashes based on the Raspberry Pi camera observations.
GLM might not detect all the CG strokes in the same flash, especially the first one or two. (see Zhang and Cummins, 2020)
GLM might not detect CG strokes with continuing currents.
GLM might not detect some CG strokes when the clouds were thick.

## Slide 38
UMD Lightning YouTube Channel
Thank you!
https://www.youtube.com/channel/UC4RfgtjUbotawHh7UzCRBAw