## Slide 1: Update on the Development and Performance of the Mid-Atlantic Lightning Mapping Array (MALMA)
Guangyang Fang, Daile Zhang
University of Maryland/CISESS
September 13, 2022
2022 GLM Science meeting

## Slide 2: Outline
Update of MALMA
Performance of MALMA
  Thunderstorm causing massive outages in College Park on 07/12/2022;
  Thunderstorm causing fatalities near the White House on 08/04/2022
Future works

## Slide 3: Update of MALMA
Due to intensive maintenance in 2021, DCLMA sites are functioning well;
In March, 2022, Dr. Tim Lang hosted a discussion about the combined MALMA processing. Given the NASA-owned Washington, D.C. LMA (DCLMA) and the NASA Wallops LMA (WFFLMA) are combined and processed as a single entity, the Mid-Atlantic LMA (MALMA), and DCLMA has some challenges with certain stations, it makes sense to perform the combined MALMA processing for a NASA-provided data product rather than creating separate DCLMA & WFFLMA products;
In April, 2022, the server which does the data processing and hosts the web pages located in northern New Mexico was pulled and moved to a safer location because the area was under mandatory evacuation for a nearby forest fire;
In July, the server was moved back to the old location;
In August, one of the WFFLMA stations in UMD_UAS had an issue with the GPS connection. After being inspected on-site, the GPS coaxial cable was found to be cut off from the end near the ground. It seemed to be bitten by some animals. After replaced with a good GPS cable, the site functioned well again.

## Slide 4: Current Status of MALMA
DCLMA (Wired) | Status | Detail | Wallops LMA (Wireless) | Status | Detail
a Sterling | Up |  | a Accomack_WESR | Up | 
b->j Woodbridge | Up |  | b THRN_Property | Up | 
c CSM | Up |  | c Wallops_Pad | Up | 
d Howard | Down | To be installed | d Plywood_Plant | Up | 
e UMD | Up |  | e Sod_Farm | Up | 
f AgSite | Up |  | f SnowHill_AB | Up | 
g GMU | Up |  | g Powerville_VFD | Up | 
h Site8 | Up |  | h UMD_UAS | Up | 
i Beltsville | Up |  |  |  | 
A wired spare unit | Ready for use |  |  |  | 
A solar spare unit | Ready for use |  |  |  | 

## Slide 5: Thunderstorm That Caused Destruction and Power Outage in College Park, MD on July 12, 2022
Destruction in Greenbelt
There were severe thunderstorms with very active lightning flashes;
MALMA detected the flashes;
The strong gust winds in the thunderstorm caused a power outage over 24 hours. College Park, Berwyn Heights, and Greenbelt were among the areas affected;
Power outages left traffic lights functionless.

## Slide 6: Thunderstorms That Caused Fatalities Near the White House on Aug 4th, 2022
At around 6:50 PM EST, three people were killed and one injured by a lightning strike in the Lafayette Square near the White House in DC;
Both MALMA and NLDN detected these flashes.
NLDN reports within 3 km
All NLDN reports

## Slide 7
NLDN reported 6 CG strokes. The strongest was the second stroke (-25.5 kA);
Both GLM and MALMA detected the flash
  MALMA detected 5/6. Missed the 1st stroke (-16.9 kA).
  GLM detected 3/6.
NLDN reported one –IC pulse right after the 1st CG stroke, but the location is fairly close to the 2nd stroke; MALMA detected sources before the 2nd stroke.

## Slide 8: Future work
Installation of a new site at Howard University in D.C.;
Relocation of site at APL/John Hopkins University due to noises;
Installation of a solar LMA site;
VR visualization of lightning data from MALMA, GLM, and other
ground-based observations.

## Slide 9: Thank you for your attention!