## Slide 1: The Effect of Ground Processing on GLM Performance
Phillip Bitzer

## Slide 2: What goes into GLM detection efficiency?
GLM performance, i.e., detection efficiency, is determined by two factors:
  Instrument performance – how well does GLM detect light
  Ground algorithms – how well does ground processing filter noise from lightning
Each contribute to what the user cares about – how much lightning is detected.
But can we improve what we have?

## Slide 3: How do we assess performance?
To assess how GLM is performing, we find GLM events that occur within the spatial-temporal bounds of a LMA flash
  Eliminates any ambiguities caused by flash grouping
Run matching on both L1b and L0
  L0 represents best possible performance with instrument (as currently configured)
  L1b represents combined instrument + ground algorithm
  Comparison of L1b and L0 yields the effect of ground processing

## Slide 4: Previous Results
We’ve reported DE using this technique before, mostly using PLT results
Consistent with other researchers, DE varies as a function of flash area and storm mode/type
But certain storm type/mode also yields low(er) DE for ground based systems
LMA Area (km2) | DE (GLM ¦ NALMA) | DE (GLM ¦ COLMA) | DE (ENI ¦ COLMA)
All | 0.617 | 0.256 | 0.372
> 8 | 0.738 | 0.365 | 0.534
> 16 | 0.806 | 0.429 | 0.609
> 32 | 0.873 | 0.522 | 0.702
> 64 | 0.922 | 0.649 | 0.797
> 100 | 0.947 | 0.746 | 0.850

## Slide 5: New Results
Now, we’ll look at a couple of cases from the Relampago campaign in Argentina, including an anomalous storm
This gives results for storms post-PLT tuning, in addition to a slightly less off-axis viewing angle

## Slide 6: 20181214 – High Flash Rate Storm
Dec 14, 2018 00Z-09Z
  MCS with max flash rate ~ 600/min and overshooting tops
  Almost 22 000 flashes detected
  LMA source altitude mode at approximately 10 km
  Analyzed in Lang et al. 2020

## Slide 7: 20181214 – High Flash Rate Storm
Area (km2) | Num LMA Flashes | Num GLM – L1b | DE – L1b | Num GLM – L0 | DE – L0
All | 20822 | 8222 | 0.395 | 12285 | 0.590
> 8 | 12651 | 6953 | 0.550 | 9494 | 0.751
> 16 | 8426 | 5472 | 0.649 | 6972 | 0.827
> 32 | 4918 | 3809 | 0.775 | 4485 | 0.912
> 64 | 2477 | 2185 | 0.882 | 2397 | 0.968
> 100 | 1414 | 1324 | 0.936 | 1399 | 0.989
Operational algorithm yields an overall DE of 40%,
yet almost 60% of the flashes were detected by the instrument
Consistent with previous results,
DE improves (significantly) with increasing flash size.

## Slide 8: 20181214 – High Flash Rate Storm
L0 detects more flashes during times when L1b struggles

## Slide 9: 20181214 – High Flash Rate Storm
While there is a dependence of DE on flash area and altitude, it is not linear. Very little light is detected for small flashes at all altitudes.

## Slide 10: 20181220 – Anomalous Storm
Dec 20, 2018 17Z-2359Z
  Anomalous charged storm (likely) with max flash rate ~ 250/min
  Almost 140 000 flashes detected
  LMA source altitude mode at 4-8 km
  Analyzed in Lang et al., 2020

## Slide 11: 20181220 – Anomalous Storm
Area (km2) | Num LMA Flashes | Num GLM – L1b | DE – L1b | Num GLM – L0 | DE – L0
All | 135956 | 62897 | 0.463 | 87888 | 0.646
> 8 | 69687 | 46506 | 0.667 | 57190 | 0.821
> 16 | 43893 | 32775 | 0.747 | 38191 | 0.870
> 32 | 24274 | 19961 | 0.822 | 22192 | 0.914
> 64 | 11940 | 10494 | 0.879 | 11304 | 0.947
> 100 | 7133 | 6430 | 0.901 | 6840 | 0.959
Again, there is almost a 20 percentage point improvement in DE!
There are decreasing gains with increasing area.

## Slide 12: 20181220 – Anomalous Storm
L0 detects more flashes during times when L1b struggles

## Slide 13: 20181220 – Anomalous Storm
While there is a dependence of DE on flash area and altitude, it is not linear. Very little light is detected for small flashes at all altitudes.

## Slide 14: Loss Fraction: 1- DE (L0)/DE (L1)
Another way to thing about it is: how much performance is “thrown out” by ground processing?
Area (km2) | DE L0 | DE L1b | Delta DE | Loss Fraction
All | 0.637 | 0.451 | 0.186 | 0.292
< 8 | 0.807 | 0.645 | 0.162 | 0.200
< 16 | 0.861 | 0.728 | 0.133 | 0.155
< 32 | 0.912 | 0.812 | 0.101 | 0.110
< 64 | 0.950 | 0.878 | 0.071 | 0.075
< 100 | 0.964 | 0.907 | 0.057 | 0.059
Almost 30% of flashes are filtered by ground processing!

## Slide 15: Does duration of the flash matter?
The L0 detections are slightly better at short duration flashes…
…but the biggest improvement is among 100-500 ms flashes.
  Note the L1b result is slightly different from Zhang and Cummins (2020), which showed a monotonic increase of DE with flash size.
Begs the question: is L0 just picking up single event flashes?
L1b
L0

## Slide 16: Does L0 matching pick up noise?
Although unlikely, an event during the time of a flash, an event in the spatial footprint of the flash could be due to noise.
However, the distribution of events per flash doesn’t change appreciably.
  Since we’re detecting more smaller/shorter flashes, some shift to fewer events/flash is expected
But since the distribution is largely similar, the L0 detections are not just single events detected during longer flashes!

## Slide 17: Ground processing affects DE!
Current ground processing throws out almost 30% of flashes that the GLM instrument detects. ﻿
If the detected light during these flashes were correctly (not) filtered, then it leads to a nearly 20 percentage point improvement in detection efficiency.
The largest gains are realized with small flashes.
The distribution of events per flash does not change appreciably.
﻿Also to note: On average, L0 detects flashes about 30 ms earlier that L1b (median: 5 ms).

## Slide 18: The next steps
So, if the GLM instrument is detecting light during flashes, but current ground processing are not classifying it correctly, then there is an opportunity to improve the end product.
Current testing of a new operational-type algorithm (i.e., satisfying ordering and latency requirements) shows at least a few percentage points improvement even in these difficult storms
  Anomalous storm 39% -> 45% overall
  Note: current iteration is unoptimized - more improvements to be realized!
See Clem’s talk Thursday!