## Slide 1: GLM Background Imagery Viewable in AWIPS
Brianna Witherell
NOAA Lapenta Intern
Mentors: Joe Zajic, Lee Byerle

## Slide 2: GOES ABI
What happens when ABI is not available to WFO’s?

## Slide 3: Background on the background imagery
Full disk image produced every ~2.5min
Uncalibrated, not geolocated
Resolution: 8km at nadir
Wavelength: 0.77 µm

## Slide 4: What is AWIPS?
Advanced Weather Interactive Processing System
NWS forecaster “battlestation”
122 Weather Offices, 13 River Centers, 9 Centers

## Slide 5: Imagery -> AWIPS
ISatSS pipeline that pulls GLM Background Image from AWS
KD Tree based resampling of GLM background imagery into 5424x5424 pixel output array
Feed resampled imagery to AWIPS for processing

## Slide 7
Hurricane Darby, Pacific Ocean (2022)

## Slide 9: Is it perfect? No. CCD subarray boundary artifacts Geolocation offset error

## Slide 10: Forecaster Impressions
01
Columbia, SC WFO
“Huh… it looks a lot like GOES-8.”
02
GLM Working Group
“I thought it would look a lot worse than that.”
03
All 5 WFO’s Surveyed
“In the event of an ABI outage, I could forecast off this imagery.”

## Slide 11: In summary
GLM background imagery is useful to NWS forecasters in event of ABI outage
Further work is needed for artifact removal and geolocation correction
Email: brianna.witherell@noaa.gov