## Slide 1: LMLEO
Detecting Lightning from Low Earth Orbit
GLM Science Meeting
02 September 2025
Jonathan Dalrymple
LMLEO Lightning Detection
© 2025 Lockheed Martin Corporation. All Rights Reserved.

## Slide 2: What is LMLEO?
LMLEO measures an essential climate variable globally across seasonal and diurnal cycles, extending the climate data record
LMLEO can observe smaller and dimmer optical sources than any lightning mapper ever flown (3x dimmer than LIS)
LMLEO’s fisheye optics provide a ground sample distance of 2.2 km at nadir (FOV average 2.6 km, 4x smaller pixel than LIS)
High Sensitivity
Global Coverage
High Spatial Resolution
Global Flash Rate Distribution
Asia remains poorly covered by GEO ring
Compare to LIS: ~7 µJ/m2/sr day ~3.3 µJ/m2/sr night
16+ LMLEO pixels cover 1 GLM pixel
1000+ km FOV for
almost 2 minutes of persistent observation
LMLEO is a new lightning mapper designed for Low Earth Orbit

## Slide 3: LMLEO Image Simulation
We have a state-of-the-art image simulation framework to model a LEO lightning mapper
Scene Flow
Background scene generation
GOES ABI Imagery
Boresight Displacement Model
LMLEO radiometric model
Simulated video
Scene Flow Model
LMLEO Image Simulation Model
Example LMLEO Image Sequence

## Slide 4: GeoXO LMX Lightning Detection Algorithm in GEO
The GeoXO LMX Real-Time Event Processor uses background and noise characteristics to determine possible lightning events
Background Estimation
Noise Estimation
Dynamic Thresholding
Possible Lightning Events
Focal Plane Array Readout
Downlink

## Slide 5: Scene Flow – “I've got a feeling we're not in GEO anymore!”
Local contrast boundaries are a problem for any real-time event processor!
Pixel Footprint
Strong Local Contrast
Oh no!
Phew!
Contrast Boundary
leads to…
Scene Flow
RTEP Limitations at a Contrast Boundary
Pixel Footprint Encounters Strong Local Contrast
Real-time processors can’t see into the future, so we can’t tell if inflection points are due to pulses (lightning) or induced by scene flow.

## Slide 6: Algorithm Adaptations for LEO
Add a recursive high-pass filter architecture?
Original
High-Pass Filter
High frequency details are not lost!
Pixel Value [DN]
Time
Recursive High-Pass Filter On Simulated LMLEO Data
Filtered Value
Portion of Previous Filtered Value
Portion of Change in Input Values
Slowly-changing slope is removed
Example Image Sequence with High-Pass Filter
But this has a few side effects:
HP filter effectively removes the background
  Lost meaning in “Pixel Value [DN]”
Requires storing 3 new values per pixel (, , )
  Large impact on memory bandwidth
: requires operations with decimal precision
  More clock cycles per pixel, per iteration
Not all hope is lost!
Recursive HP filter tells us that there is value in modeling the medium-term change in the input values to suppress contrast boundaries’ effects on the RTEP algorithm

## Slide 7: Algorithm Adaptations for LEO
Estimation of the background slope reduces the effects of scene flow on the RTEP algorithm!
Background Estimation
Noise Estimation
Dynamic Thresholding
Possible Lightning Events
Focal Plane Array Readout
Downlink
By estimating slope, we can reduce the effect scene flow has on the background state
BG Slope Estimation

## Slide 8: LMLEO Path Forward
Maturation of the instrument design in parallel with LMX
  Funded partially by Lockheed Martin IRAD
Orbit selection
  575 km altitude, 45.4° inclined orbit is affordably accessed by SpaceX Bandwagon ride share
Investigate teaming possibilities and mission scope
  Instrument only or full mission?
  Deliver hardware or deliver data?
  How best to fund the effort?
We are eager to build a team and support behind LMLEO!

## Slide 9: Thank You
© 2025 Lockheed Martin Corporation. All Rights Reserved.