## Slide 1: Ground-based radiometry for source-constrained optical modeling
Eric Bruning, Kelcy Brunner, Stephanie Weiss, Sam Gardner (TTU)
Thom Edwards, Belle Storm, Lydia Wermer (Sandia)
This work supported by the GOES-R and GEO-XO programs under a NOAA Cooperative Institute Task 3 project through CIWRO. Thanks to ENTLN and NLDN for providing data as part of GLM cal/val.
GLM Science Meeting
2 Sep 2025, Online

## Slide 2: Talk outline
GLM Science Meeting
Overview of field site, instruments, sample count
  Thanks to ENI and NLDN via cal/val agreement for data, and GLM cal/val and GEOXO funding
Four case examples
  Even in four flashes, lots of combinations of mutual detection, providing a good test.
  Delta E for each stroke
  Will get stroke energy, cloud optical depth, etc. from Sandia
Synthesis plans
  Can we covary observed source energy with observed GLM using a simple
  Consistent signal that 337 precedes 777
Next steps/concluding remarks
  Cloud modeling of cases and optical transport of well-characterized
  Reminder brag about dataset size
  Happy to share LMA and slow antenna for ground network comparisons

## Slide 3: 2025 dataset
Instruments
Continuous regional measurements:
  West Texas LMA, GLM-E/W, GLM-East; ENI and NLDN; KLBB WSR-88D.
At TTU Reese Center Field site:
  Sandia Radiometer at 337, 777, 150 and 320-1110 nm
    Calibrated to watts at radiometer aperture
    200 ksps, with triggered context camera
    View is to NNE
  TTU electric field change “slow” antenna, 100 ms time constant, 10 ksps
    Calibration in process
Radiometer
field of view FOV

## Slide 4: 2025 dataset
392 total radiometer triggers
Slow antenna on each day, usually 1-3 at Reese site.
  Distributed 8-station network across Lubbock for a tornadic supercell and multicell storms on two days, but storms to east of radiometer FOV.
Numerous supercell and multicell cases, some disorganized lines of storms
Radiometer trigger counts |  | 
Date | Count | Herein
4/26/2025 | 74 | 
4/30/2025 | 3 | 
5/6/2025 | 2 | 
5/25/2025 | 1 | 
5/27/2025 | 1 | 
6/2/2025 | 1 | 
6/3/2025 | 2 | 2 –CG
6/5/2025 | 1 | 
6/24/2025 | 1 | 1 +CG
6/30/2025 | 1 | 
7/8/2025 | 5 | 1 –CG
7/21/2025 | 89 | 
7/22/2025 | 1 | 
7/23/2025 | 210 | 
Next slides: some examples close to field site with clear context camera images of CGs

## Slide 5
C
Colored pixels: GLM-E total optical energy
Green dots / lines: GLM groups
Other dots: West Texas LMA channels
B
C
A
Obs
Site
3 June 2025, 02:14:09 UTC: four –CGs
Obs
site
-23, -19, -23, -11 kA
–CGs at A, B, C, D at two ground strike points. C, D are subsequent strokes of B.
All detected by radiometer and GLM-W.
A, C: Not detected by GLM-E.
B, D: Detected by GLM-E.
Perhaps dart leader activity on positive channels at 6-7 km altitude explains GLM-E difference.
Largest electric field change at times of CGs, with slow electrostatic change continuing after last stroke during IC processes.
B
C
A
yes
no
GLM-W
radiometer
ΔE
GLM-E
D
D
no
yes
A
BCD
A
BCD
0.2 ms
B
A
0.2 ms
No radiometer amplitude during
continued illumination in second camera frame.
First camera frame (0.1 s, A-D)
A
BCD
2nd cam frame
1st cam frame
GLM-E: no
GLM-E: yes
777 nm
337 nm
777 nm
337 nm

## Slide 6
E,F,G
Colored pixels: GLM-E total optical energy
Green dots / lines: GLM groups
Other dots: West Texas LMA channels
B
C
A
Obs
Site
3 June 2025, 02:16:26 UTC: six –CGs
Obs
site
-10, -17, -17, -19, -7, -10 kA
–CGs at A, C, D, E, F, H, at three ground strike points.
Every radiometer pulse and CG detected by GLM-W.
A, B: Not detected by GLM-E.
Camera did not trigger on A, D, which were dimmer: more obscured by precip.
E, F are first and subsequent strokes. G may be misclassified, since ΔE is sharp. F and G have multi-pulse optical structure over several ms. H is in between second and third camera frames.
Many additional electric field change episodes corresponding to GLM-W , likely all from dart processes on positive leaders.
GLM-W
radiometer
ΔE
GLM-E
D
Much brighter
AD
EFH
20 ms
B
C
D
E
F
G
H
A
E
F
G
H
yes
yes
yes
yes
yes
yes
no
no
dim
~dim
C
AD
EFH
C
E
-19 kA CG
F
-7 kA CG
G
-6 kA IC
E
1 ms
777 nm
337 nm

## Slide 7
+25 kA stroke to ground
C
Colored pixels: GLM-E total optical energy
Green dots / lines: GLM groups
Other dots: West Texas LMA channels
B
C
B
C
A
A
Obs
Site
24 June 2025, 04:00:28 UTC: +CG
B
C
A
Obs
site
Three 25 kA +CGs at A, B, C from an extensive charge region in stratiform cloud.
LMA channels span about 50 km
Cloud/rain optical depth modifies the intensity of optical pulses observed at 777 nm by GLM and a radiometer at ground.
A: Moderately bright from GLM, but too far from radiometer observing site at TTU.
B: Very bright from GLM, just barely observable at radiometer through rain at 45 km range; might be cloud illumination due to FOV.
C: Moderately bright from GLM, very bright at radiometer at 15 km range; camera confirmation of ground strike.
(Left): three peaks at 777 during CG; peaks at 337 with first and last peak.
Largest electric field change at times of CGs.
B
C
A
dim
bright
bright
mod
mod
none
GLM-W
rad.
ΔE
smoothed due to site noise
GLM-E
2 ms
777 nm
337 nm

## Slide 8
Colored pixels: GLM-E total optical energy
Green dots / lines: GLM groups
Other dots: West Texas LMA channels
B
C
B
C
A
A
Obs
Site
8 July 2025, 06:22:45 UTC: –CGs
-15, -17, -9 kA CG strokes at A, B, C
Cloud/rain optical depth modifies the intensity of optical pulses observed at 777 nm by GLM and a radiometer at ground at about 10 km range.
A: Undetected by GLM-E, W but obvious in radiometer. Optically thicker cloud?
Intracloud event between A, B observed by GLM, radiometer
B, C: Both strokes clearly visible in all instruments. On the southern edge of convective core, so perhaps a better scattering path.
D: Apparent intracloud dart leaders without ground network detection. Only seen from GLM-W. About 20 ms of weak 777 pulses seen at radiometer. Slower field change as charge is rearranged in cloud.
2 ms
Obs
site
A
B
C
A
dim
bright
dim
mod
no
mod
GLM-W
rad.
ΔE
Square wave pattern is instrument artifact
GLM-E
B
C
D…
bright
no
Bright, mod
dim
B
777 nm
337 nm

## Slide 9: Pulse Analysis
Expected results: 337 nm band peak prior to 777 nm
Actual Observations: 337 nm band peak prior to all other bands*
  *The 337 nm band matched the peak time of the wide band in the 7/08/2025 event
Peak Times (relative, µs) |  |  |  | 
Band | 6/3/2025 02:14:09 | 6/3/2025 02:16:27 | 6/24/2025 04:00:29 | 7/08/2025 06:22:45
337 nm | 20 | 20 | 35 | 40*
777 nm | 35 | 45 | 50 | 50
1570 nm | 50 | 60 | 65 | 100
320-1100 nm | 25 | 45 | 35 | 40*

## Slide 10: Future work
Large-sample quantitative testing of optical scattering
Quantitatively test if radiometric measurements plus clouds structure can predict observed energy in space.
  During CGs strokes, how much additional light is emitted within the cloud?
Explain why weaker optical pulses aren’t observed by current GLMs
  Assess needed sensitivity of future instruments such as GEO-XO LMX.
After calibration, create an open dateset with DOI for slow antenna and LMA data.
Calibrated
Radiometry
LMA + stroke source location
Source energy at 777 nm
GLM E
energy at 777
vs.
GLM W energy at 777
Homogeneous and heterogeneous cloud optical depth
WRF-ELEC
microphysics
Depth of cloud along path from radar
Daily cloud variability
Obs of CGs with well-characterized source
Space obs
+
+
Predict energy emitted to space

## Slide 11
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.